## Slide 1: Synchronous Collaborative Control of Dual-SCARA Systems
A Lagrangian Dynamics and Optimization-Based Approach
Research & Implementation Framework
December 2025

## Slide 2: I. Introduction & Industrial Context
● Modern Manufacturing: High-cycle sorting and precision assembly.
● SCARA Units: Ideal for planar compliance and vertical rigidity.
● Collaborative Leverage: Utilizing dual robots to double effective throughput.
● Research Focus: Achieving zero-latency mirroring and optimized linear paths.

## Slide 3: II. Critical Problem Statement
● Synchronization Lag: Communication bottlenecks in Master-Slave relay.
● Trajectory Arcing: Natural joint interpolation creates nonlinear arcs.
● Workplace Safety: Collision risks in shared zones during high-speed sync.
● Mathematical Mapping: Heterogeneous base offsets in global world frames.

## Slide 4: III. Research Objectives
● Modeling: Derive full Lagrangian EOM and Analytical IK.
● Control: Implement leader-follower synchronous reflection logic.
● Optimization: Solve constrained trajectory via Lagrange Multipliers.
● Validation: High-fidelity sub-millisecond physics in Gazebo/ROS 2.

## Slide 5: IV. Forward & Inverse Kinematics
Forward Kinematics (FK):
x = L1 cos(θ1) + L2 cos(θ1 + θ2)
y = L1 sin(θ1) + L2 sin(θ1 + θ2)
Inverse Kinematics (AIK):
θ2 = arccos((x² + y² - L1² - L2²) / (2L1L2))
θ1 = atan2(y, x) - atan2(L2 sinθ2, L1 + L2 cosθ2)

## Slide 6: V. Jacobian & Singularity Analysis
Jacobian Matrix Relationship:
v = J(q) q̇
Singularity Condition:
det(J) = L1 L2 sin(θ2) = 0
Optimized Solution (DLS Pseudo-inverse):
J† = Jᵀ (JJᵀ + k²I)⁻¹

## Slide 7: VI. Lagrangian System Dynamics
Equations of Motion:
τ = M(q)q̈ + C(q, q̇)q̇ + G(q)
● M(q): Mass/Inertia Matrix deriving dynamic link coupling.
● C(q, q̇): Coriolis and Centrifugal force vectors.
● G(q): Gravity vector (Prismatic joint compensation only).

## Slide 8: VII. Trajectory Optimization (MIS)
Objective: Minimize f(q̇) = ½ q̇ᵀ q̇ (Joint Velocity Norm)
Constraint: J q̇ - v_desired = 0 (Linear Cartesian Path)
Lagrange Solution:
q̇* = Jᵀ(JJᵀ)⁻¹ v_target
● This ensures perfectly straight motion with minimal energy consumption.

## Slide 9: VIII. Synchronous Mirroring Framework
● Master Node: Solves task and broadcasts Cartesian targets.
● Replication Manager: Intercepts and transforms targets.
Mirroring Reflection Matrix:
P_slave = [1 0; 0 -1] P_master_rel
● Ensures perfect geometric symmetry relative to conveyor centerline.

## Slide 10: IX. ROS 2 / Gazebo Implementation
● Loop Frequency: 100 Hz (Real-time trajectory publishing).
● Physics Loop: 1000 Hz (High-fidelity contact simulation).
● Communication: ROS 2 Humble logic gates & action servers.
● Control: Position-based PID with Lagrangian feed-forward terms.

## Slide 11: X. Experimental Validation & Results
● IK Solver Latency: 0.32 ms (Avg).
● Linear Path Error: < 0.001 m (Numerical precision match).
● Throughput: Increased from 12 to 22 blocks/minute (+83%).
● Capture Success: 98.5% in collaborative handover trials.

## Slide 12: XI. Conclusion & Significance
● Proved that Lagrangian optimization yields safer industrial paths.
● Mirrored systems provide immediate horizontal scaling for sorting.
● MIS Unit-1 Principles (Lagrange) successfully applied to real robotics.
● Framework is scalable to N-robot swarm coordination.

## Slide 13: Thank You!
Questions & Discussions
Contact: [Your Email]